Power System Report
System overview
- Solar Arrays
  - Specs
- Batteries
  - http://www.batteryspace.com/prod-specs/4315.pdf
- Beta Angle
  - Critical Beta Angle
- Eclipse Times
  - durations
- power Generation
  - Max and Min beta angle
  - Charge time
- power budget
- Simulation Details

Simulation Details
STK Scenario, 6 Aug 2019 16:00:00 - 6 Aug 2020 16:00:00

3d model – Lassat_V1_stk_Aug12.dae
Orbit – 400 km circular, I = 51.6446 deg (assume ISS orbit), step size 60 s
J2 Perturbation

Attitude: Aligned and constrained,
Aligned ref vector Selfie-Sat Nadir (centric) (0,0,-1)
Constrained ref vector Selfie-Sat velocity (1,0,0)

Beta Angle and Eclipse Times:

Default Time period, step size (60 s) for plot

Table of values in Appendix
bold%beta^c = sin^-1[ {R} over {R+h}] 0<=bold%beta^c<=90 (1) critical beta angle, Space Thermal Control Handbook, Volume 1 – Gilmore, David G. - 2002. Page 41 equation 2.8

bold%beta^c = sin^-1[ {6378} over {6378+400}] = 70.217^o

Eclipse-free intervals are:
 Start: 9644820 epoch sec, Finish: 9968580 epoch sec, duration = 3.747 days
 Start: 14828400 epoch sec, Finish: 14953140 epoch sec, duration = 1.444 days
 Start: 27718620 epoch sec, Finish: 28152000 epoch sec, duration = 5.016 days

Calculated eclipse fraction with:
f_E = {1} over {180^o} cos^-1[{ sqrt{h^2+2Rh} } over{(R+h)cos%beta} ]

found that lighting conditions are favourable

worst case: 39% of orbit in eclipse
best case: 0% of orbit in eclipse (intervals are above)
average: 34.3% of orbit in eclipse

orbital period is 73 minutes

worst case: 28.47 minutes of eclipse, 44.53 minutes of light
average: 25.039 minutes of eclipse, 47.961 minutes of light

lighting interval sim in STK to verify:

Max B - “Lighting Times” Report/Graph for 22 Jun 00:00:00 to 28 Jun 00:00:00 shows approximately 5 days of lighting (matches calculation for lighting intervals above beta angle)

Min B - Report/Graph for 11 Aug 2019 00:00:00 to 12 Aug 2019 00:00:00 (one of several minimum beta angle time periods) shows a total of 33815.572 seconds in umbra. 33815.572/86400 = 0.3913 which verifies the calculation for worst case 39% in eclipse.

Solar Cells